## Slide 1: Darcy’s Law - Introduction
CE 544 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Darcy’s Experiment
Darcy did some lab tests on flow through sand in 1856

## Slide 3: Darcy’s Law
Darcy experimented with different soils and with different values of L, h1, and h2. The results showed that:
where:
q = DVol/Dt = flow rate [L3/T]
k = coefficient of permeability
or hydraulic conductivity [L/T]
A = gross cross-sectional area of flow [L2]
h = total head [L]
L = length of flow path [L]

## Slide 4: Alternate Formulation
Darcy's law is often written as:
q = kiA
where
i = hydraulic gradient
where s is the flow path length

## Slide 5: Darcian vs. Seepage Velocity
Darcy's law can be rewritten as:
q = kiA
vd = ki
vd = "discharge velocity" or "Darcian velocity"
Vs
Vd
vs = "seepage velocity"

## Slide 6: Seepage Velocity
Seepage velocity can be related to discharge velocity as follows:
Vv = Volume of soil voids
V = Total volume
n = porosity

## Slide 7: Seepage Velocity, cont.
n | vs/vd
0.33 | 3
0.5 | 2
0.67 | 1.5
0.75 | 1.3
n =
total area
area

## Slide 8: Effective Porosity
Not all voids in the soil conduct flow.
ne = "effective" porosity
where Af = actual area of flow

## Slide 9: Effective Porosity, cont.
ne = ln
l = effective porosity factor
l is determined experimentally
l  1 for sands and gravels
l = 0.01 - 0.5 for clays

## Slide 10: Typical Values of K
http://en.wikipedia.org/wiki/Hydraulic_conductivity