## Slide 1: Limit Equilibrium Procedures Part 2
CE 544 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: General Method of Slices
Unknowns:
    1 factor of safety
    n values of N
    n locations for N
    n-1 values of E
    n-1 values of X
    n-1 locations for E
Total: 5n-2
Equilibrium Equations:
    n equations for SFv=0
    n equations for SFH=0
    n equations for SM=0
Total: 3n
5n-2 > 3n, therefore statically indeterminate
S = f(c’,f’,u,N,F,Dl)

## Slide 3: General Method of Slices
Note: side forces can be represented by magnitude and direction. Same number of equations and unknowns.

## Slide 4: General Method of Slices
Several techniques based on method of slices
Each technique uses a different set of assumptions to reduce # of unknowns
Some techniques satisfy complete equilibrium
  2n-2 assumptions
  3n equations satisfied
Some don’t satisfy equilibrium
  >2n-2 assumptions
  <3n equations satisfied

## Slide 5: Ordinary Method of Slices

## Slide 6: Ordinary Method of Slices (OMS)
Key assumption  Side forces can be neglected (i.e., sum to zero on each slice)
S Forces perpendicular to base of slice:
General equation:
Substituting s:
Notes: Some of these equations have been converted to MS OFFICE equation format. I had a problem with the lower case L displaying properly. Would like to switch everything to MS Office format eventually.

## Slide 7: Ordinary Method of Slices
If f = 0:
0
 This is the same solution we found earlier for the generalized method

## Slide 8: Ordinary Method of Slices
For effective stress analysis:
 This equation can lead to unrealistically low or even negative effective stresses (unconservative)

## Slide 9: Ordinary Method of Slices
Alternate Formulation
Define vertical effective weight:
S forces perpendicular to base:
Substituting:
This is the preferred formulation for OMS

## Slide 10: Summary - OMS
Circular shear surface
Only satisfies moment equilibrium
For f=0, OMS gives the same solution as the Swedish method
F can be calculated directly, without iteration
Less accurate than other procedures of slices

## Slide 11: Simplified Bishop’s Method

## Slide 12: Simplified Bishop’s Method
Simplifying assumption:
Side forces are horizontal. I.e., vertical side force components (Xi, Xi+1) are equal to zero.

## Slide 13: Simplified Bishop’s Method
S forces in the vertical direction:
Substituting:

## Slide 14: Simplified Bishop’s Method
Solving for N:
From general equation (based on moment equilibrium):

## Slide 15: Simplified Bishop’s Method
Combining the three previous equations and solving for F:
For total stress analysis:
Note that F is on both sides. Must be solved iteratively.

## Slide 16: Simplified Bishop’s Method
For f=0, equation reduces to:
Which is the same equation derived for log spiral, Swedish method, and OMS

## Slide 17: Simplified Bishop’s Method
Once F is found, N can be computed as:
For OMS:
Difference in solution is due to differences in N. Both use the same overall equation:

## Slide 18: Summary – Simplified Bishop’s
Unknowns:
    n normal forces along base of slice
    1 factor of safety
Total: n+1
Equilibrium Equations:
    n equations for SFv=0
    1 equation for overall SM=0
Total: n+1

## Slide 19: Summary – Simplified Bishop’s
Circular slip surface
Horizontal side forces
Satisfies
  Moment equilibrium
  Force equilibrium in vertical direction
More accurate than OMS, especially for effective stress analysis with high pore pressures

## Slide 20: Bishop’s Complete Equilibrium Procedure
Similar to simplified procedure except it is not assumed that all (Xi+1 – Xi) = 0.
A set of values for vertical side forces is assumed and vertical and horizontal force equilibrium is checked. Process is repeated until equilibrium is satisfied.
Time-consuming and complicated

## Slide 21: Force Equilibrium Procedures

## Slide 22: Force Equilibrium Procedures
Can be used on non-circular surfaces
No attempt is made to satisfy moment equilibrium

## Slide 23: Force Equilibrium Procedures
Unknowns:
    1 factor of safety
    n values of N
    n-1 values of Z
    n-1 values of q
Total: 3n-1
Equilibrium Equations:
    n equations for SFv=0
    n equations for SFH=0
Total: 2n
3n-1 > 2n, therefore n-1 assumptions necessary
Best strategy is to assume n-1 values of q
Since we are not satisfying moment equilibrium, locations no longer matter

## Slide 24: Force Equilibrium Procedures
Procedure
(1) Assume F, compute:

## Slide 25: Force Equilibrium Procedures
(2) Start on slice #1. Solve for N and Z by satisfying SFx=0 and SFy=0.

## Slide 26: Force Equilibrium Procedures
(3) Repeat for each of the slices in sequence:

## Slide 27: Force Equilibrium Procedures
(4) Forces should balance on the last slice:
2 equations
1 unknown
If forces do not balance, try a new F and repeat steps 2-4

## Slide 28: Side Force Assumptions
Lowe and Karafaith
  For each slice, use average slope of ground surface and slip surface
Simplified Janbu
  The side forces are assumed to be horizontal
U.S. Army Corps of Engineers
  Parallel to slope (see next slide)

## Slide 29: Side Force Assumptions, Cont.
U.S. Army Corps of Engineers
“Modified Swedish Procedure”

## Slide 30: Summary – Force Equilibrium Methods
Works on both circular and non-circular surfaces
Satisfies force equilibrium only, not moment equilibrium
Requires iteration
Key assumption = side force inclinations

## Slide 31: Complete Equilibrium Procedures

## Slide 32: Complete Equilibrium Procedures
Unknowns:
    1 factor of safety
    n values of N
    n-1 values of E
    n-1 values of X
    n locations for N
    n-1 locations for E
Total: 5n-2
Equilibrium Equations:
    n equations for SFv=0
    n equations for SFH=0
    n equations for SM=0
Total: 3n
We need 2n-2 assumptions to make the problem statically determinate
Assume n locations of normal forces, N (middle of slice). This leaves n-2 assumptions still required

## Slide 33: Spencer’s Method
Simplifying assumption:
All side forces are parallel. (=constant)
Unknowns:
    1 factor of safety
    n values of N
    n-1 values of Z
    1 side force inclination q
    n-1 locations of Z
Total: 3n

## Slide 34: Spencer’s Method
Side forces Zi and Zi+1 are combined into a single resultant side force Qi, acting at an angle = q.

## Slide 35: Spencer’s Method
He also assumed that W,S, and N all act through the same point b (center of the bottom of the slice)
Therefore, Qi must also act through the same point b in order to maintain moment equilibrium

## Slide 36: Spencer’s Method
For overall moment equilibrium:
(same as before)

## Slide 37: Spencer’s Method
Since Q acts through b, Q must be equal to sum of W, S, and N. Therefore, work in terms of Q.
Two components of Q:
(perp. to base)
(parallel to base)
S Moments (in terms of Q):

## Slide 38: Spencer’s Method
For overall force equilibrium:
Since q = constant, both simplify to:

## Slide 39: Spencer’s Method
By summing forces on individual slices, you can derive equation for Q in terms of known quantities:
Now we have two equations:
And two unknowns:
F and q
Once again, equations must be solved iteratively.

## Slide 40: Spencer’s Method
Non-circular surfaces:
Set up a coordinate system and sum moments about the origin
Once again, we have two equations and two unknowns.

## Slide 41: Morgenstern & Price Method
Interslice shear force is related to interslice normal force by:
The normal force N acts at the base of the slice
Satisfies complete equilibrium
More work than Spencer’s method, but gives about the same results
l = unknown scaling factor
f(x) = assumed function

## Slide 42: Chen & Morgenstern’s Method
Improvement to M&P method.
Interslice shear force is related to interslice normal force by:
Equation is thought to better represent side force relationship at ends
Satisfies complete equilibrium

## Slide 43: Sarma’s Procedure
Similar to M&P and C&M methods
Interslice shear force is related to shear strength as follows:
Developed for applications in seismic stability and includes seismic coefficient
Satisfies complete equilibrium

## Slide 44: Comparison of Methods
See tables 6.2 and 6.3 in text
Spencer’s method is often the preferred method
  Accurate
  Simplest complete equilibrium method
  Can be used for circular or non-circular surfaces