## Slide 1: Seismic Slope Stability Analysis
CE 544 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Introduction
Seismic slope stability should be evaluated for all slopes in seismically active regions
Earthquakes affect stability in two ways:
  Reduced shear strength
  Increased forces driving failure due to ground motion/horizontal acceleration

## Slide 3: San Fernando Quake, 1971
Lower San Fernando Reservoir
Strength reduction due to liquefaction
Notes: http://cabierta.uchile.cl/revista/8/seismic.html

## Slide 4: San Fernando Quake, 1971

## Slide 5: Introduction, Cont.
Two main types of analysis:
  Comprehensive approach
  Simplified (pseudo-static) approach
ShihKang Dam – Taiwan
Damaged in 921 Quake in 1999

## Slide 6: Comprehensive Approach, Cont.
Involves a finite element analysis of stresses and strains caused by acceleration time history. Resulting pore pressures and strengths are fed into limit equilibrium analysis to compute FS.

## Slide 7: Pseudostatic Analysis
Earthquake loading is represented by a static force = k*W through center of gravity where k is a seismic coefficient
K is typically 0.05-0.25

## Slide 8: Infinite Slope

## Slide 9: Infinite Slope, cont.

## Slide 10: Ordinary Method of Slices (OMS)
(a = moment arm for kW)

## Slide 11: OMS – Compare Equations
Original:
Modified:

## Slide 12: Bishop’s Simplified Procedure
Original:
Modified:

## Slide 13: Pseudostatic Screening
Seismic Slope Stability Analysis

## Slide 14: Pseudostatic Screening Analyses
Useful method for screening sites that are not expected to lose a large amount of strength during an earthquake
Components
  Reference peak acceleration, aref
  Acceleration multiplier
  Shear strength reduction factor
  Minimum factor of safety
  Tolerable permanent deformation

## Slide 15: 1) Peak Acceleration, aref
Two cases typically analyzed:
  10% probability of exceedance (PE) in 50 years
  2% probability of exceedance (PE) in 50 years
Typically expressed as a fraction of gravity (aref/g)
Either the peak bedrock acceleration (PGArock) or the peak acceleration at top of slope (PGAsoil) determined from dynamic response analysis
PGArock can be found from: http://earthquake.usgs.gov/hazards/

## Slide 16
Notes: https://earthquake.usgs.gov/static/lfs/nshm/conterminous/2014/2014pga10pct.pdf

## Slide 17
Notes: https://earthquake.usgs.gov/static/lfs/nshm/conterminous/2014/2014pga2pct.pdf

## Slide 18: PGA for Specific Locations
https://earthquake.usgs.gov/hazards/interactive/

## Slide 19
Click here to find lat/lon
Pick your return period here

## Slide 22
Click on alternate return period above and plot will refresh

## Slide 23: Determining k factor
Where:
  aref/g = peak acceleration
  a/aref = acceleration multiplier
Acceleration multiplier is a scaling factor. Typically ~0.5 (see Table 10.1 in text)

## Slide 24: 3) Shear strength reduction factor
Makdisi and Seed (1977) found that non-liquefiable soils undergo small strains under cyclic loads when loaded to less than 80% of static strength
Thus, most experts recommend that static strength should be reduced by 0.8 when performing seismic analysis

## Slide 25: 4) Minimum factor of safety
(see table 10.1 in text)
Acceptable factor of safety for seismic analysis
Ranges from 1.0-1.15

## Slide 26: 5) Tolerable displacement
(see table 10.1 in text)
Maximum displacement expected if previous components are utilized/honored in the analysis
Ranges from 0.15-1.0 m

## Slide 27: Shear Strengths
New Slopes – Short term (immediately after construction)
  Total stress analysis
  Unconsolidated-undrained tests
Existing Slopes – Long term (after equilibrium)
  Total stress analysis
  Unconsolidated-undrained tests
New Slopes – Long term (after equilibrium)
  Use consolidated-undrained strengths
  Two approaches
    Two-stage analysis (similar to rapid drawdown)
    Simplified procedure

## Slide 28: Two-Stage Analysis
Similar to rapid drawdown approach
First stage
  Based on static (pre-earthquake) conditions
  Used to compute s’fc and tfc on failure surface.
Second stage
  Effective stresses from stage 1 are used to find undrained shear strength, tff.
  FS is computed using tff and loading conditions corresponding to earthquake (kW force added)

## Slide 29: Simplified Procedure
Analysis is done in one step
Strengths are defined using R-envelope
  FS is computed using loading conditions corresponding to earthquake (kW force added)
Even though the strengths from the R-envelope are undrained, pore pressures corresponding to pre-earthquake conditions must be used in order to ensure that proper effective stresses are found and fed into the R-envelope equation.

## Slide 30: R-Envelope
Comparable to the tff vs. s’fc curve used in rapid drawdown (the d-y curve), but a little more conservative. See figure 10.6 in text