## Slide 1: Factors of Safety and Reliability
CE 544 – BRIGHAM YOUNG UNIVERSITY
Notes: From Duncan and Wright, Chapter 13

## Slide 2: Factor of Safety
S = shear strength of soil
t = shear stress required for equilibrium
Traditional definition:
But what does that mean in practice? What does F=1.3 mean?
Notes: F=1.01 would be fine if we had complete certainty in our analysis
The most uncertain part of analysis is shear strength – so we can say that F=1.3 means that we can reduce S by 30% and still be OK.

## Slide 3: What value of FS is acceptable?
 | Uncertainty of Analysis Conditions | 
Cost and consequence of failure | Small | High
Cost of repair comparable to cost of building more conservative slope | 1.25 | 1.5
Cost of repair much greater than cost of building more conservative slope | 1.5 | 2.0+
 | Required Factors of Safety |  | 
Types of slopes | End of Construction | Long-Term Steady Seepage | Rapid Drawdown
Slopes of dams, levees, dikes, and other embankment and excavation types | 1.3 | 1.5 | 1.0-1.2
US Army Corps of Engineers Slope Stability Manual
Notes: Guidelines like this should only be used when the methods of site testing, analysis, etc. are consistent from one project to the other.

## Slide 4: Reliability and Probability of Failure
R = 1 - Pf
Where:
  R = Reliability
  Pf = Probability of failure
Alternative measure of analyzing stability
Reliability = the probability that the slope will perform as designed and not fail over the life of the project
Notes: Talk about impact of using reliablity vs factor of safety. Public/clients sometimes don’t want to know that there is some probability of failure.

## Slide 5: Reliability and Uncertainty
In order to determine reliability, we need to understand the uncertainty in each of the input parameters.
Primary uncertainty relates to shear strength (c, f), but there may be a range of uncertainty in other parameters also (g, u, etc.)
Uncertainty is typically represented by standard deviation (s) or coefficient of variation (COV)

## Slide 6: Standard Deviation
Where:
n = number of samples
xi = individual sample values
xave = average sample value

## Slide 7: Coefficient of Variation
Typically expressed as a percentage (Ex. 0.23  23%)
See spreadsheet for sample calculations

## Slide 8: Frequency Histogram
Chart: Su [psf]
| 120.56349849835391 | 151.41821876995925 | 182.2729390415646 | 213.12765931316994 | 243.98237958477529 | 274.83709985638063 | 305.69182012798598 | 336.54654039959132 | 367.40126067119667 | 398.25598094280201 | 429.11070121440736 | 459.9654214860127 | 490.82014175761805 | 521.67486202922339 | 552.52958230082868 | 583.38430257243408 | 614.23902284403948 | 645.09374311564477 | 675.94846338725006 | 706.80318365885546
120.56 151.42 182.27 213.13 243.98 274.84 305.69 336.55 367.40 398.26 429.11 459.97 490.82 521.67 552.53 583.38 614.24 645.09 675.95 706.80 | 2 | 1 | 1 | 4 | 3 | 11 | 14 | 18 | 17 | 23 | 27 | 22 | 18 | 15 | 12 | 7 | 2 | 2 | 0 | 1
Mean = 400, s = 100, N = 200

## Slide 9: Frequency Histogram
Freq.
Parameter Value
s
Mean
If we have enough samples, we can calculate the mean and standard deviation directly from our dataset.
However, we rarely have enough samples to adequately characterize the mean and standard deviation with confidence. Therefore, we typically infer the values using one of the methods in the following slides

## Slide 10: 3s Rule
99.7% of all values fall within +/- 3 standard deviations
If you can estimate the max and min expected values, you can estimate the standard deviation as:

## Slide 11: 3s Rule, cont.
See in-class exercise for sample calculations
Studies have shown that even experts often under-estimate max and min values (estimated range is typically too small)
Thus, it is conservative to estimate the standard deviation as:

## Slide 12: Graphical Method
Steps:
Draw average line
Draw max and min line
Draw +/- s lines assuming 3s rule (or 2s to be conservative)
Notes: Figure 13.1 Example of graphical 3sigma rule for undrained strength profile.

## Slide 13: Graphical Method
Notes: Figure 13.2 Example of graphical 3sigma rule for shear strength envelope.

## Slide 14: Typical COV Ranges

## Slide 15: Reliability Analysis

## Slide 16: Determining Reliability
We typically assume that F is log-normally distributed
Overall reliability can be determined once we know the following values:
  FMLV = Factor of safety for slope using most likely values (averages)
  COVF = Coefficient of variation for factor of safety

## Slide 17: Probability of Failure vs FMLV, COVF

## Slide 18: Probability of Failure vs FMLV, COVF
(same as previous table)
Notes: Figure 13.3 Probabilities of failure based on lognormal distribution of F.

## Slide 19: Reliability Equation
Values in previous table and figure can be found using equations.
Reliability index (b) = Number of standard deviations between FMLV and verge of failure (F=1).
Lognormal Reliability Index:
You can then use bLN as in input argument to the Excel function NORMSDIST() to compute the reliability.
R=NORMSDIST(bLN)

## Slide 20: Determining Reliability
FMLV is found using conventional slope stability analysis
In order to determine reliability, we need to find COVF
Two common approaches:
  Monte Carlo Method
  Taylor Series Method

## Slide 21: Monte Carlo Method
Generate N equally likely model “instances” or “realizations” by randomizing model parameters in a systematic fashion
Run all N models and calculate F for each model
Calculate COVF

## Slide 22: Parameter Randomization
c
f
g
# | c | f | g
1 | 235 | 21.4 | 118.3
2 | 241 | 23.7 | 115.9
3 | 276 | 28.2 | 117.8
4 | 199 | 25.0 | 123.6
5 | 212 | 25.8 | 121.0
6 | 205 | 27.3 | 115.7
7 | 249 | 23.7 | 113.8
8 | 251 | 19.9 | 119.2
9 | 225 | 27.1 | 116.7
10 | 299 | 26.1 | 112.7
11 | 189 | 24.4 | 120.3

## Slide 23: Standard Deviation
# | c | f | g | F
1 | 235 | 21.4 | 118 | 1.42
2 | 241 | 23.7 | 116 | 1.28
3 | 276 | 28.2 | 118 | 1.17
4 | 199 | 25 | 124 | 1.05
5 | 212 | 25.8 | 121 | 0.89
6 | 205 | 27.3 | 116 | 1.23
7 | 249 | 23.7 | 114 | 1.04
8 | 251 | 19.9 | 119 | 1.19
9 | 225 | 27.1 | 117 | 1.30
10 | 299 | 26.1 | 113 | 1.10
11 | 189 | 24.4 | 120 | 0.95
Mean F = 1.15
sF = 0.159
COVF = 0.159/1.15 = 13.9%
How many runs are required?
Ideally, you would do enough model runs to achieve “statistical convergence”; i.e., the point at which doing additional model runs only makes a minor difference in the mean F.

## Slide 24: Taylor Series Method
  Determine si for each parameter
  Find Fi+ and Fi- for each parameter where
    Fi+ = F with parameter value = MLV+ si and all other parameters held constant
    Fi- = F with parameter value = MLV- si and all other parameters held constant
  Compute DFi = |Fi+ - Fi-| for each parameter
Method for estimating the COVF using a parameter sensitivity analysis
Steps:

## Slide 25: Taylor Series Method, cont.
  Compute sF and COVF as follows:

## Slide 26: Case Study – San Francisco LASH Terminal (1970)
Failure occurred over a 250 ft long stretch of trench during excavation.

## Slide 27: LASH Terminal, cont.
See spreadsheet for reliability calculations

## Slide 28: Alternative Designs